## Slide 1: CCSv6 Fundamentals Workshop for CC2650
Lab Handbook

## Slide 2: Outline
Lab Requirements and Setup
Lab 1A: Getting Started: LCD SmartRF06EB Example
Lab 1B: More Basics: LCD SmartRF06EB Example
Lab 2: Basic Debug: Pin Interrupt Example
Lab 3A: Real-time Debug: LCD SmartRF06EB Example
Lab 3B: ROV: LCD SmartRF06EB Example
Lab 4: Multi-target Debug: Per Test Example

## Slide 3: LAB Requirements
Software:
  Code Composer Studio v6.1.0 or greater
    With all Wireless Connectivity components installed
  TI-RTOS for SimpleLink Wireless MCUs
  Per Test package
Hardware:
  CC2650EM-7ID with SmartRF06EB
    Device rev PG 2.2+
    Lab 4 requires two such targets!
USB JTAG Connection
Power Switch

## Slide 4: LAB Material Notes
It is assumed the main workshop directory is located in C:\ccsv6_workshop\cc2650\workspace
It is assumed that that Per Test is installed in C:\ccsv6_workshop\cc2650\per_test
The lab material will make references to these directory
If the lab material is located in a different location, please update the path to reflect your environment

## Slide 5: LAB Conventions
Before starting, it is important to review some lab conventions that will ease your work…
Lab steps are in black and numbered for easier reference
  …
  …
Explanations, notes, warnings are written in blue
  Warnings are shown with
  Information is marked with
  Tips and answers are marked with
  Questions are marked with
Notes: 5

## Slide 7: Lab 1A: Getting Started: LCD SmartRF06EB Example 15 minutes
Notes: 7

## Slide 8: LAB 1A: Exercise Summary
Key Objectives
  Import and build the LCD SmartRF06EB example program
  Start a debug session and load/flash the program to the target
  Run the program
Tools and Concepts Covered
  Workspace
  Resource Explorer
  Building example projects
  Running example projects
Notes: 8

## Slide 9: Launch CCS and Open Resource Explorer
Double click on the Code Composer Studio desktop icon
Specify C:\ccsv6_workshop\cc2650\workspace as the workspace location
Select Browse Examples in the Getting Started page

## Slide 10: Resource Explorer: Examples
Displays all example projects discovered by the Resource Explorer
Step by step instructions on how to build/run the examples
Select the LCD SmartRF06EB example under TI-RTOS for SimpleLink Wireless MCUs -> SimpleLink Wireless MCU -> CC2650F128 –> Driver Examples -> TI Target Examples -> LCD Examples

## Slide 11: Step 1: Import LCD SmartRF06RB Project
Follow Step 1 and import the LCD SmartRF06RB project into the CCS Workspace by clicking on the Import the example project into CCS link

## Slide 12: Step 1: Import LCD SmartRF06RB Project
The project will appear in the Project Explorer if the import is successful and a green checkmark will appear next to the link to indicate success

## Slide 13: Step 2: Build LCD SmartRF06RB Project
Follow Step 2 and build the LCD SmartRF06RB project by clicking on the Build the imported project link
The build Console view will appear along the bottom with build messages as the project builds
If the build is successful, a green checkmark will appear next to the link to indicate success

## Slide 14: Step 3: Specify Debugger Configuration
Note that a green checkmark exists for Step 3 since the Connection type is already defined
  The emulator connection is already specified in the project properties and a target configuration was generated on project import (Step 1)

## Slide 15: Step 4: Debug LCD SmartRF06RB Project
Follow Step 4 and debug the project by clicking on the Debug the imported project link
Several actions are done automatically
  Prompt to save source files
  Build the project (incrementally)
  Start the debugger (CCS will switch to the CCS Debug perspective)
  Connect CCS to the target
  Load (flash) the program on the target
  Run to main
Don’t want it to do all of the above at once? You can configure it to skip some steps (Debugger Options)

## Slide 16: Debug Session for LCD SmartRF06RB Project
Program counter at main
Switched to CCS Debug perspective
Debug view for project being debugger
Target execution toolbar
Debug messages in the Console view
Notes: 16

## Slide 17: Run LCD SmartRF06RB Program
Press the Resume button (in the target execution toolbar) to run the program
  Program will run and text will be displayed to the LCD
Press the Suspend button to halt the target
Press the Terminate button to terminate the debugger
  This will terminate the debug session and switch back to the CCS Edit perspective
Notes: 17

## Slide 18: LAB1A: Summary
In this lab we completed the following:
  Used the Resource Explorer to import build and debug the LCD SmartRF06EB example
Notes: 18

## Slide 20: Lab 1B: More basics: LCD SmartRF06EB Example 15 minutes
Notes: 20

## Slide 21: LAB 1B: Exercise Summary
Key Objectives
  Use the Memory Allocation view to determine code size usage
  Analyze the advice from the Optimizer Assistant in the Advice view
  Enable optimization in the Project Properties
  Get familiar with Simple Mode
Tools and Concepts Covered
  Memory Allocation view
  Optimizer Assistant
  Advice view
  Project Properties
  Simple Mode
Notes: 21

## Slide 22: View: Memory Allocation
Open the Memory Allocation view via View -> Memory Allocation
  The Memory Allocation view is a graphical display of the memory allocation of the program
  Note the total allocation size in FLASH
Numbers may vary slightly in your environment
Notes: 22

## Slide 23: Advice View
Maximize the Advice view in the lower right corner by double-clicking on the tab for the window
  The Advice view provides advice on how to better optimize the code for size/performance/power
Expand the Optimization Advice node and resize the Description column so that the advice is more visible
Note the third advice, on how optimization is disabled and level 3 optimization is recommended, and double-click on it
  Double-click on the advice itself and not on the hyperlink (#27007-D)
23

## Slide 24: Project Properties
The Project Properties dialog will be opened to the compiler optimization settings
  Options such as compiler/linker settings, pre/post build steps, and project dependencies can be set from this dialog
  The dialog can also be opened by right-clicking on a project in the Project Explorer view and selecting Properties
Compiler Options
Linker Options
Device and high level settings

## Slide 25: Project Properties
Change the Optimization level to 3
Press OK to apply the changes and exit the dialog
Double-click on the Advice window tab to restore the Advice window back to the original size
Note optimization ‘speed vs size trade-off’ setting favors smaller code size

## Slide 26: Debug vs Optimization Tradeoff
The higher the level of optimization (speed/size/power), the greater the negative impact in debug visibility/experience
Trade-off between the ease of debugging and the effectiveness of compiler optimization
Best trade-off point depends on user preference… but usually the lowest level of optimization which meets your system constraints
  Use the lowest optimization setting if debug visibility is the highest priority (debugging difficult bugs in application behavior)
Some impact on the debug experience for highly optimized code:
  Source-line setting is erratic (code has been removed/rearranged)
  Unable to set source-line breakpoints (code has been removed/rearranged)
  Unable to view certain variables (variables optimized out)
For more details:
  http://processors.wiki.ti.com/index.php/Debug_versus_Optimization_Tradeoff

## Slide 27: Switch to Simple Mode
Select the option to enable Simple Mode in the Getting Started page (View -> Getting Started)
This will switch the perspective to the CCS Simple perspective
27

## Slide 28: Simple Mode
Simple Mode is a simplified Perspective that combines the key views and menus of the CCS Edit and CCS Debug perspectives into one view for those that want a simpler interface and wish to avoid the constant Perspective switching
28
Debug view
Project Explorer view

## Slide 29: Debugging in Simple Mode
Use the Debug button to rebuild, load and run the program to main
Press the Resume button to run the program
  Check LCD on target to confirm program is running correctly
Note that there is no perspective switch in Simple Mode

## Slide 30: View: Memory Allocation
Open the Memory Allocation view via View -> Other… -> Code Composer Studio -> Memory Allocation
  The Memory Allocation view is hidden in the default Simple Mode perspective, hence the need to go to View -> Other…
Note the total allocation size in FLASH
  Code size for FLASH decreased after optimization is enabled
Numbers may vary slightly in your environment
Notes: 30

## Slide 31: Clean Up
Press the Suspend button to halt execution
Terminate the Debug Session
Disable Simple Mode in the Getting Started page (View -> Getting Started)
  The rest of the workshop will not use Simple Mode but instead use the default CCS Edit and CCS Debug perspectives

## Slide 32: LAB 1B: Summary
In this lab we completed the following:
  Became familiar with the Memory Allocation view
  Used Optimizer Assistant and the Advice view to help optimize the program
  Became familiar with Project Properties
  Became familiar with Simple Mode
Notes: 32

## Slide 34: Lab 2: basic debug: Pin Interrupt Example 30 minutes
Notes: 34

## Slide 35: LAB 2: Exercise Summary
Key Objectives
  Debug the Pin Interrupt example
  Basic Profiling
Tools and Concepts Covered
  Basic Debug
  Breakpoints/Watchpoints
  Event Counters
Notes: 35

## Slide 36: Resource Explorer: Pin Interrupt Example
Open Resource Explorer via View -> Resource Explorer (Examples)
Select the Pin Interrupt example under TI-RTOS for SimpleLink Wireless MCUs -> SimpleLink Wireless MCU -> CC2650F128 –> Driver Examples -> TI Target Examples -> PIN Examples
Follow the steps to import, build and debug the project

## Slide 37: Run Pin Interrupt Program
Press the Resume button to run the program
  This example uses interrupts to toggle LEDs 1-4 when one of the directional (or SELECT) button(s) are pressed
Play with the example by pressing the directional/SELECT buttons and observe the behavior of the LEDs
Notes: 37

## Slide 38: Debugging: Using Breakpoints
Press the Suspend button to halt execution
Set a breakpoint on line 102 of pinInterrupt.c by double-clicking in the editor margin
Press the Resume button to run the program again
Press any of the directional (or SELECT) button
Note that the target will be halted at the breakpoint location
Double-click on the breakpoint to remove it
The default behavior is to use a software breakpoint unless the program address is in a memory region known to the debugger as read-only memory (as in this case) by the debugger memory map
Notes: 38

## Slide 39: Debugging: Using Watchpoints
A Watchpoint is a type of breakpoint that monitors activity at a memory address
In this step we will halt the CPU only when the LEFT button is pressed by setting a watchpoint to halt the CPU
Hover your mouse cursor over the Board_KEY_LEFT macro on line 103 an wait for the tool tip pop-up to get the value of the macro
If the tool tip pop-up is not appearing, try double-clicking the macro to highlight it and hover over it again
Notes: 39

## Slide 40: Debugging: Using Watchpoints
Highlight pinId, right-click and select Breakpoint -> Hardware Watchpoint in the context menu
Notes: 40

## Slide 41: Debugging: Watchpoints
Right-click on the watchpoint in the Breakpoints view and select Breakpoint Properties in the context menu
Modify the properties to match the settings in the screenshot below
Hit OK to apply changes
Notes: 41

## Slide 42: Debugging: Using Watchpoints
Run the target again
Press any directional/SELECT button on the SmartRF06 board except for the LEFT directional button (note the LEDs toggling based on the button pressed)
Press the LEFT directional button and note how the target will halt at line 99 of pinInterrupt.c
Hover the mouse cursor over pinId and note the value in 0xF (hex)
Remove the watchpoint using the Remove All Breakpoints button
Notes: 42

## Slide 43: Debugging: Counting Events
Run the target again
Set breakpoints on line 96 and 100 of pinInterrupt.c by double-clicking in the editor margins
Press any directional/SELECT button on the SmartRF06 board
Note that the target has halted at the first breakpoint
Notes: 43

## Slide 44: Debugging: Counting Events
Set event counters from the Breakpoints view
Set a event counter to count cycles
Right-click on the event counter in the Breakpoints view and select Breakpoint Properties in the context menu
Enable the Reset Count on Run option in the properties dialog
Press OK

## Slide 45: Debugging: Counting Events
Run the target again
The target will halt at the second breakpoint and the event counter will display the number of cycles executed since the last breakpoint
Remove the event counter and breakpoints by using the Remove All Breakpoints button
Notes: 45

## Slide 46: More Debugging (Review)
Investigate other debugging views (Open via View menu)
  Memory Browser
  Registers
  Modules
  Disassembly (see next slide)
Notes: 46

## Slide 47: View: Disassembly
Press the Restart button to restart the program
  Program should be at main
Open the disassembly view by going to View -> Disassembly
  You can see the current location of the PC (small blue arrow) and any breakpoints (small blue circles)
Toggle the Show Source button
  Note the toggling of interleaved source with the disassembly
Notes: 47

## Slide 48: Clean Up
Remove all breakpoints from the Breakpoints view (if any)
Terminate the Debug Session

## Slide 49: LAB 2: Summary
In this lab we completed the following:
  Learned how to use breakpoints and watchpoints
  Learned how to count events (cycles)
  Became familiar with the Disassembly view
Notes: 49

## Slide 51: Lab 3A: REAL-TIME DEBUG: LCD SmartRF06EB Example 15 minutes
Notes: 51

## Slide 52: LAB 3A: Exercise Summary
Key Objectives
  Demonstrate how to access memory in real time when processor is running
Tools and Concepts Covered
  Real-time access to memory
  Continuous refresh in views
Notes: 52

## Slide 53: Editing the Source Code
Open lcdSmartRF06EB.c source file in the editor (if not already opened) by double-clicking on the file in the Project Explorer (under the lcdSmartRF06EB_CC2650F128 project)
Insert the following code:
  Line 53: uint32_t gCounter = 0;
  Line 163: gCounter = counter;
Use the Debug button to rebuild, load and run the program to main
  Make sure the lcdSmartRF06EB_CC2650F128 project is selected (has context)!

## Slide 54: Adding Variables to the Expressions View
Right-click on gCounter on line 53 of lcdSmartRF06EB.c and select Add Watch Expression… to add it to the Expressions view

## Slide 55: Adding Variables to the Expressions View
Right-click on gCounter in the Expressions view and select View Memory
  The Memory Browser will open to the location of gCounter

## Slide 56: Continuous Refresh
Run the target
Enable Continuous Refresh in both the Expressions view and Memory Browser view
See the values update while the target is running
Halt the target

## Slide 57: Clean Up
Restart the program with the Restart button
Leave the application at main for the next lab

## Slide 58: Real-Time Access: Summary
After completing this lab you should now be familiar with:
  Real-time memory accesses with CCS
  How to enable Continuous Refresh in a view
Notes: 58

## Slide 60: Lab 3B: ROV 45 minutes
Notes: 60

## Slide 61: LAB 3B: Exercise Summary
Objectives
  Get familiar with using ROV (RTOS Object View) to inspect state of the scheduler, threads and objects in the system
Tools and Concepts Covered
  RTOS Object Viewer (ROV)
Notes: 61

## Slide 62: Open the RTOS Object View (ROV)
ROV can be used to inspect state of the scheduler, threads and objects in the system
Go to menu Tools -> RTOS Object View (ROV) to open ROV
In RTOS Object View expand lcdSmartRF06EB_CC2650F128.out

## Slide 63: Use ROV
Click on Task to see details of tasks in the system
  Check the state of each task (and their stacks) in the system
Answer the following for each task:
  What are the priorities and current states/mode?
  What is the size of stack and stack peak? (Hint: some info is in Detailed tab)

## Slide 64: Use ROV
Click the Resume button to run the program
Let it run for ~5 seconds, then click the Suspend button to halt Answer the following for each task again:
  What are the current states/mode?
  What is the stack peak?

## Slide 65: Clean Up
Click on the Terminate button in the Debug view More information on ROV is available at: http://rtsc.eclipse.org/docs-tip/RTSC_Object_Viewer

## Slide 66: Exercise Summary
After completing the labs you should be familiar with:
  Using ROV (RTOS Object View) to inspect state of threads in the system.
Additional References:
  TI-RTOS Users Guide: http://www.ti.com/lit/spruhd4
  SYSBIOS Wiki: http://processors.wiki.ti.com/index.php?title=Category:SYSBIOS

## Slide 68: Lab 4: multi-target deBug: Per Test Example 45 minutes
Notes: 68

## Slide 69: LAB 4: Exercise Summary
Key Objectives
  Create a single custom target configuration file for two CC2650F128+SmartRF06EB targets
  Learn the basic concepts of:
    Target configurations
    Project-less debugging
    Multi-target debugging
Tools and Concepts Covered
  Target Configurations view
  Advanced Target Configuration Editor
  Starting a project-less debug session
  Working with executables generated from other tool chains
  Specifying debug source search paths
  Multi-target Debug
NOTE: This lab requires two targets (CC2650EM-7ID+SmartRF06EB)
Notes: 69

## Slide 70: Create a Target Configuration File
Open the Target Configurations view (View -> Target Configurations)
Specify 2_CC2650F128.ccxml as the File name
Ensure that Use shared location is enabled
Hit Finish when done
  The Target Configuration Editor will be opened

## Slide 71: Target Configuration Editor
Set/Enter the following:
  Connection: Texas Instruments XDS100v3 USB Emulator
  Board or Device search field: 2650 (Select CC2650F128 from the remaining list)
Click on the Target Configuration link to go to the Advanced editor

## Slide 72: Target Configuration Editor (Advanced)
Press the New… button to add a new connection type
Select Texas Instruments XDS100v3 Emulator in the list of Connections
Press Finish

## Slide 73: Target Configuration Editor (Advanced)
The new connection has been added
Press the Add… button to add a device
Select Cortex M in the filter list and select CC2650F128 in the list of Devices
Press Finish

## Slide 74: Target Configuration Editor (Advanced)
A CC2650F128 device has been added to the new connection and now there are two XDS100v3 connections, each with a CC2650F128 device, configured for this single target configuration
But how does CCS know which XDS100v3 connection applies to which board?
XDS100 emulators can be identified by their serial numbers!

## Slide 75: Getting the Serial Numbers for XDS100
Open a command window and browse to the following location:
  <CCSv6 INSTALL DIR>\ccsv6\ccs_base\common\uscif
Run the following command:
  > xds100serial
All XDS100 connections to the host will be scanned and listed with their serial numbers

## Slide 76: Target Configuration Editor (Advanced)
Select the Texas Instruments XDS100v3 USB Emulator_0 node in the left pane
For the Connection Properties, change the Emulator Selection setting to Select by serial number and then enter the first serial number found by the xds100serial utility
Repeat steps 1 and 2 above for XDS100v3 USB Emulator_1 using the other serial number detected
Press Save to save the configuration

## Slide 77: Launch the Debugger
Right-click on 2_CC2650F128.ccxml under the User Defined node in the Target Configurations view and choose Launch Selected Configuration
The debugger will be launched – this is known as a project-less debug session since it was originally launched without a project association

## Slide 78: Launch the Debugger
A single debug session for BOTH SmartRF06 boards will have started
Note how there are two CPUs that are now visible in the Debug view – one for each CC2650F128 CPU found on the two separate emulator connections

## Slide 79: KNOWN ISSUE WITH GROUPS (1)
The rest of the lab steps relies on GROUPS (each M3 core is combined into a single group)
There is a known stability issue with CCSv6.1.0 when trying send a run/resume command to the group
  This issue will be resolved in CCSv6.1.1
It is recommended to avoid group level commands (when the group is selected in the Debug view) and send commands individually to each core by manually selecting each node under the group (have to manually repeat the action for each core)
The group (Group 1) is selected above and any debugger command will be issued to the group (group level command)
The first core (or node under core) in the group is selected and any debugger command will be issued to just the first core

## Slide 80: KNOWN ISSUE WITH GROUPS (2)
Another option is to simply skip groups all together and always keep the cores separate in the Debug view
  Send commands individually to each core by manually selecting each node
The fix for this bug will be available in the next CCS update (6.1.1)
No group created and cores kept separate

## Slide 81: Creating Groups
Multi-select the both sub-nodes in the Debug view (press CTRL and then click on each node) and right-click to bring up the context menu
Select Group core(s)
This will group the selected nodes under a new node that represents the group
The group can be selected to broadcast commands to all members of the group
Selecting Group 1 will change the debug context to the whole Group

## Slide 82: Working with Groups
Select the Group 1 node in the Debug view and press the Connect Target button to connect to both targets
Select the Group 1 node in the Debug view and press the Load button
In the Load Program dialog, specify the per_test.out program located in:
  C:\ccsv6_workshop\cc2650\binary
  This will load the program on to both targets
Select the Group 1 node in the Debug view and press the Resume button to run the program on both targets

## Slide 83: Working with Groups
Both targets will begin running and the LCD should indicate that the CC2650 PER TEST is running
Feel free to play with the PER test example if desired (see PER test documentation)

## Slide 84: Multi-Emulator/Target Debug
CCS treats a multi-emulator debug session the same a single emulator debug session for a multi-core device
Each CPU in the debug session has its own debug context and can be controlled separately
  When a CPU has debug context, all actions apply to that CPU and all views display data for that CPU
Groups can be used to control multiple CPUs at once (broadcast commands)

## Slide 85: Multi-Core Debug
Select the Group 1 node in the Debug view and press the Suspend button to halt execution of both targets
Select the Group 1 node in the Debug view and press the Restart button to restart the program for both targets
Expand the node for the first CPU under Group 1, to expose the call stack, and select the top entry in the call stack
Select Locate File… to browse to the location of main.c (C:\ccsv6_workshop\cc2650\ per_test\source)
Selecting the first CPU will change the debug context to the first CPU

## Slide 86: Breakpoints
Open the Breakpoints view (View -> Breakpoints)
Open the Disassembly view (View -> Disassembly)
In the Disassembly view: Type in menu in the address field and select menuButtonCb in the list of suggestions
  The Disassembly view will jump to the address of menuButtonCb

## Slide 87: Breakpoints
In the Disassembly view: Scroll down to address 0x68A8 and double-click in the margin to set a breakpoint
  This location is reached when the SELECT button is pressed on the SmartRF06RB
  This will set a breakpoint for just the first CPU
Contents of Disassembly view is for current debug context (first CPU)

## Slide 88: View Breakpoints by Debug Context
In the Breakpoints menu, select Group by -> 4 Debug Contexts
Which CPU does this breakpoint apply to?
Breakpoints are now grouped by debug context (CPU) for easy identification
Notes: 88

## Slide 89: Breakpoints – Run Program
Select the Group 1 node in the Debug view and press the Resume button to run the program on both targets
Press the Select button on the SmartRF06 board which represents the first CPU
Note how the first CPU will be halted at the breakpoint while second CPU continues to run

## Slide 90: Clean Up
Halt the target
Remove all breakpoints from the Breakpoints view (if any)
Terminate the Debug Session

## Slide 91: Multi-Core Target: Summary
After completing this lab you should now be familiar with:
  Creating Advanced Target Configuration files
  Working with a multi-core debug session
  Working with Debug Groups
  Working with multiple debug contexts
  Working with Breakpoints in a multi-core environment
Notes: 91