## Slide 2: Objectives
Describe how interrupts work in general and on each architecture
Learn how to configure TI-RTOS Hwi’s for each architecture (similar and different)
Explain how to nest interrupts using TI-RTOS
Compare/contrast kernel-managed interrupts with the interrupt keyword (non-BIOS)
Lab – Add an Hwi to respond to a timer interrupt that blinks the LED

## Slide 3: Outline
Hardware Interrupts (Hwi)
How Interrupts Work
Configuring an Hwi
Managing ISRs – Two Ways
Hwi Benchmarks
Lab

## Slide 4: SYS/BIOS Thread Types (including Tasks)
Priority
Hwi
Hardware Interrupts
Hardware event triggers Hwi to run
BIOS handles context save/restore, nesting
Hwi triggers follow-up processing
Priorities set in silicon
Swi
Software Interrupts
Software posts Swi to run
Performs Hwi ‘follow-up’ activity (process data)
Up to 32 priority levels (16 on C28x/MSP430)
Task
Tasks
Usually enabled to run by posting a ‘semaphore’ (a task signaling mechanism)
Designed to run concurrently – pauses when waiting for data (semaphore)
Up to 32 priority levels (16 on C28x/MSP430)
Idle
Background
Runs as an infinite while(1) loop
Users can assign multiple functions to Idle
Single priority level
Hwi and Idle – in code...
Notes: Using Clock Fxns in a Task-based video system is not really recommended because Clock Functions will ALWAYS have a higher priority than TSKs because periodic functions s are prioritized as Swis.

## Slide 5: Foreground / Background Scheduling
main()
{ init
while(1)
nonRT }
ISR get buffer process printf()
main() { init BIOS_start() }
Scheduler
Hwi get buffer process LOG_info1()
Idle nonRT + instrumentation
Idle events run in sequence when no Hwis are posted
Hwi is ISR with automatic vector table generation + context save/restore
Hwi performs “process” – typical use is to perform HRT need, then post “follow-up activity”

## Slide 6: Outline
Hardware Interrupts (Hwi)
How Interrupts Work
Configuring an Hwi
Managing ISRs – Two Ways
Hwi Benchmarks
Lab

## Slide 7: How do Interrupts Work?
2. Sets a flag in a register
. . .
UART
GPIO
Timers
Ext pins
Etc.
An interrupt occurs
How are interrupts "enabled"?

## Slide 8: Receiving Interrupts (with BIOS Functions)
IER
“Individual Enable”
GIE
“Master Enable”
CPU
IFR
Interrupt Flag
0
1
0
UART
Interrupt Enable Reg (IER) turns on individual ints
Hwi_disableInterrupt();
Hwi_enableInterrupt();
GPIO
etc …
Interrupt Flag Reg (IFR)
bit set when int occurs
Hwi_post();
Hwi_clearInterrupt()
Global Interrupt Enable (GIE) Enables ALL IER-enabled interrupts
Hwi_enable()
Hwi_disable()
Hwi_restore()
Note: Hwi_post() not supported on MSP430
Notes: Uint32 gie;
…
gie = IRQ_globalDisable();
...
IRQ_globalRestore(gie);

## Slide 9: How do Interrupts Work?
3. CPU acknowledges interrupt and …
  Stops what it is doing
  Turn off interrupts globally
  Clears flag in register
  Saves return-to location
  Determines which interrupt
  Calls ISR
2. Sets a flag in a register
. . .
4. ISR (Interrupt Service Routine)
  Saves context of system*
  Runs your interrupt code (ISR)
  Restores context of system*
  Continues where it left off*
* Must be done in user code, unless you use SYS/BIOS
UART
GPIO
Timers
Ext pins
Etc.
An interrupt occurs

## Slide 10: Outline
Hardware Interrupts (Hwi)
How Interrupts Work
Configuring an Hwi
Managing ISRs – Two Ways
Hwi Benchmarks
Lab

## Slide 11: Configuring an Hwi – Statically via GUI
1
Use Hwi module (Available Products) , insert new Hwi (Outline View)
Example:
Tie Tiva Timer2A to the CPU’s HWI5
2
Configure Hwi – Event ID, CPU Int #, ISR vector:
Remember, BIOS objects can be created via the GUI, script code or C code (dynamic)
User can configure:
  Handle – name of object
  ISR fxn (e.g. myTickFxn)
  Interrupt number (from datasheet, e.g. Timer2A = 39)
  Priority & Event Id (arch-specific)
  Enable at startup (IER)
  Masking options (nesting) (more later)
Let's look at each device's Hwi config - one at a time...

## Slide 12: Hwi Configuration – Tiva & MSP430
Tiva - C
Interrupt number comes from datasheet
Interrupt Priority specifies Priority Group:
0x00 (0), 0x20 (1), …, 0xe0 (7) = default “-1”
Event Id: Shown but NOT applicable
MSP430
Interrupt number comes from datasheet
Interrupt Priority and Event Id are not used

## Slide 13: Hwi Configuration – Tiva & MSP430
Tiva - C
Interrupt number comes from datasheet
Interrupt Priority specifies Priority Group:
0x00 (0), 0x20 (1), …, 0xe0 (7) = default “-1”
Event Id: Shown but NOT applicable
MSP430
FR5969
Interrupt number comes from header file:
Interrupt Priority and Event Id are not used

## Slide 14: Hwi Configuration – C28x & C6000
C28x
Interrupt number comes from PIE table:
Interrupt Priority and Event Id not used
BIOS can auto acknowledge PIE interrupts INT1.7 equates to “38” in BIOS Hwi
C6000
Interrupt number (User INTs #4-15)
Interrupt priority – N/A
Event Id comes from datasheet:
Nesting interrupts...

## Slide 15: Nesting – Enabling Preemption of Hwi
Default mask is “SELF” – which means all other Hwi’s can pre-empt it except for itself (i.e. BIOS allows nesting by default).
Can choose other masking options as required:
ALL: Best choice if ISR is short & fast (does not work on M4)
NONE: Dangerous – make sure ISR code is re-entrant (no M4)
BITMASK: User can choose specific interrupts to nest (no M4)
LOWER: Masks any interrupt(s) with lower priority (ARM only)
Note: BIOS does not support nested interrupts for MSP430
Notes: Note: See .s62 file for vector table. For DSP (C6000, C28x, any NON-ARM device), “LOWER” compiles to “SELF” – so it is not supported. However, “LOWER” does make sense for ARM devices (M3, Cortex-A8, etc). For M4, only SELF and LOWER are supported.

## Slide 16: Outline
Hardware Interrupts (Hwi)
How Interrupts Work
Configuring an Hwi
Managing ISRs – Two Ways
Hwi Benchmarks
Lab

## Slide 17: Using the BIOS Hwi Dispatcher
Using interrupts withOUT BIOS...
currently_executing_code
{
interrupt occurs
next_line_of_code
}
Vector Table
void myHwi(arg)
{
READ_HW_PORT;
Swi_post();
}
BIOS Hwi Dispatcher
Easy to use, simple, RECOMMENDED
Turned ON for every BIOS Hwi
Slight increase in latency due to full context save/restore
Allows BIOS Scheduler function calls
Saves code space (all INTs share common save/restore routine)
Performs “smart return” – returns to highest priority pending thread
Hwi Dispatcher:
Context Save
Context Restore
“Smart” Return

## Slide 18: Using the interrupt Keyword
Summary...
currently_executing_code
{
interrupt occurs
next_line_of_code
}
Vector Table
interrupt myHwi(void)
{
context save; //nest?
READ_HW_PORT;
Process; //??
Swi_post();
context restore;
}
Interrupt Keyword
Compiler handles context save/restore
Call a function? Then full context is saved
Nesting interrupts is MANUAL
Users canNOT call any BIOS Scheduler functions (e.g. Swi_post)
Use ONLY if absolute minimum latency is required in your system (and then, just maybe)

## Slide 19: Interrupt Creation Summary
BIOS Hwi Dispatcher
  Allows nesting of interrupts
  Saves code space
  Required when ISR uses BIOS scheduler functions
  Performs a smart return to highest priority pending thread
Interrupt Keyword
  Slight advantage (only if absolute MIN latency required)
Notes:
  Choose HWI dispatcher OR Interrupt keyword on an interrupt-by-interrupt basis
  Caution:
    For each interrupt, use only one of these two interrupt context methods

## Slide 20: Outline
Hardware Interrupts (Hwi)
How Interrupts Work
Configuring an Hwi
Managing ISRs – Two Ways
Hwi Benchmarks
Lab

## Slide 21: Interrupt Response Time
 | C28x | MSP430 | Tiva-C
Non-BIOS-Mg’d | 30 | 25 | 25
BIOS-Mg’d (MIN) | 193 | 32 | 101
BIOS-Mg’d (DEFAULT) | 226 | 96 | 114
~CPU Cycles from trigger to first line of ISR code:
“Non-BIOS Mg’d” means interrupt not managed by BIOS (vector must be “plugged” manually)
Application test code (from author) run from FLASH (some wait states)
“DEFAULT” means that the default services for the interrupt are selected (mostly ALL of them).
Users can improve cycle count by turning off some features and/or running from RAM (see “MIN” numbers, where all BIOS features are turned off)
Published “interrupt latency” numbers in BIOS Benchmarks describe the longest time interrupts are disabled anywhere in the O/S.
Benchmark projects available in the \TI_RTOS folder
How do you create a "zero latency" interrupt ?

## Slide 22: Non-BIOS Managed INT Creation
Easiest of them all – simply define the INT in the CFG file and choose Priority Group ZERO
Then use interrupt keyword for the ISR:
TM4C
Cannot define “zero latency” interrupt in the BIOS GUI
User must manually use #pragma to “plug” the vector and then use the interrupt keyword:
MSP430
Define “zero latency” interrupt in the BIOS GUI (Hwi  Advanced, Ex: 0x10 is INT5):
C28x
Cannot define “zero latency” interrupt in the BIOS GUI
User must use Hwi_plug() to “plug” the vector table + Hwi_eventMap() for EventId
C6000
Hwi_plug(5, (Hwi_PlugFuncPtr)isr_nonBIOS);
Hwi_eventMap(5, 64);

## Slide 23: Outline
Hardware Interrupts (Hwi)
How Interrupts Work
Configuring an Hwi
Managing ISRs – Two Ways
Hwi Benchmarks
Lab

## Slide 24: Labs 5-9 “Roadmap”
Lab | Trigger | Hwi | Other | Fxn
5 | h/w timer | BIOS Hwi ledToggle |  | 
5B | BIOS timer ledToggle (Hwi) |  |  | 
6 | h/w timer | BIOS Hwi | BIOS Swi ledToggle | 
7 | BIOS Clock ledToggle (Hwi, Swi) |  |  | 
8 | h/w timer | BIOS Hwi | BIOS Task ledToggle | 
9 | h/w timer | BIOS Hwi | LED State → Mbx/Que →ledToggle | 

## Slide 25: Lab 5 – “Blink LED” Using Hwi
main() {
init_hw();
Timer (500ms)
BIOS_start();
}
main.c
Hwi
Scheduler
Idle
ledToggle() {
toggle(LED);
Log_info();
}
Procedure
Create a new BIOS project (min)
Add/link files (main.c, driverlib/folder)
Add Hwi object (for timer interrupt)
Build, “Play”, Debug
Add UIA/SA to project and cfg/use
Use Log_info() to print #toggles
[Optional] – use BIOS Timer module
Time: 30 min
0:00
Hwi ISR
Lab Goal:
Set up a timer in TI-Ware and configure an Hwi to respond to that timer interrupt

## Slide 27: SYS/BIOS Hwi APIs
Other useful Hwi APIs:
Can one interrupt preempt another?
Hwi_disableInterrupt() Set enable bit = 0
Hwi_enableInterrupt() Set enable bit = 1
Hwi_clearInterrupt() Clear INT flag bit = 0
Hwi_post() Post INT # (in code)
Hwi_disable() Global INTs disable
Hwi_enable() Global INTs enable
Hwi_restore() Global INTs restore
New in SYS/BIOS
IER
IFR
GIE

## Slide 28: Outline
MainHighlight
MainNormal
SubHighlight
SubNormal