## Slide 2: Objectives
Understand how Swi’s complement Hwi’s
Describe how to configure Swi’s
Detail how Swi’s are scheduled
Touch on Scheduling Strategies
Lab 6 – Use Swi to perform “Blink LED” instead of an Hwi.

## Slide 3: Outline
Using Swi
Intro
Scheduling Rules
Swi – Configuration
Other Useful APIs
Scheduling Strategies - FYI
Lab

## Slide 4: Outline
Using Swi
Intro
Scheduling Rules
Swi – Configuration
Other Useful APIs
Scheduling Strategies - FYI
Lab

## Slide 5: SYS/BIOS Thread Types (including Tasks)
Priority
Hwi
Hardware Interrupts
Hardware event triggers Hwi to run
BIOS handles context save/restore, nesting
Hwi triggers follow-up processing
Priorities set in silicon
Swi
Software Interrupts
Software posts Swi to run
Performs Hwi ‘follow-up’ activity (process data)
Up to 32 priority levels (16 on C28x/MSP430)
Task
Tasks
Usually enabled to run by posting a ‘semaphore’ (a task signaling mechanism)
Designed to run concurrently – pauses when waiting for data (semaphore)
Up to 32 priority levels (16 on C28x/MSP430)
Idle
Background
Runs as an infinite while(1) loop
Users can assign multiple functions to Idle
Single priority level
Using Hwi and Swi together…
Notes: Using Clock Fxns in a Task-based video system is not really recommended because Clock Functions will ALWAYS have a higher priority than TSKs because periodic functions s are prioritized as Swis.

## Slide 6: Hardware and Software Interrupt System
Hwi
Fast response to INTs
Min context switching
High priority for CPU
Limited # of Hwi possible
Swi
Latency in response time
Context switch
Selectable priority levels
Scheduler manages execution
TI-RTOS Kernel provides for Hwi and Swi management
TI-RTOS Kernel allows the Hwi to post a Swi to the ready queue
Execution flow for flexible real-time systems:
INT !
Hard R/T Process
Post Swi
Cleanup, RET
Continue Processing ...
Swi Ready
Hwi
*buf++ = *XBUF;
cnt++;
if (cnt >= BLKSZ) {
Swi_post(swiFir);
cnt = 0;
pingPong ^= 1;
}
Scheduling Swi's...
isrAudio:
Swi

## Slide 7: Outline
Using Swi
Intro
Scheduling Rules
Swi – Configuration
Other Useful APIs
Scheduling Strategies - FYI
Lab

## Slide 8: Scheduling Rules
Hwi
swi_a (p1)
Idle
swi_b (p2)
Highest Priority
Lowest Priority
Running
Ready
Legend
Swi_post(mySwi) : Unconditionally post a software interrupt (in the ready state)
If a higher priority thread becomes ready, the running thread is preempted
Swi priorities from 1 to 32 (MSP430/C28x has 16)
Automatic context switch (uses system stack)
time
Swi_post(swi_b)
What if the Swi's are at the same priority?
Smart return from Hwi
Notes: This diagram shows two task of unequal priority. First the lower priority task is running and is interrupted by an ISR which then runs a higher priority task. The lower priority task running is preempted and rescheduled. After the higher priority task is completed it prompts the lower priority task to run

## Slide 9: Scheduling Rules
Hwi
swi_a (p1)
Idle
swi_b (p1)
Running
Ready
Legend
Processes of same priority are scheduled first-in first-out (FIFO)
Having threads at the SAME priority offers certain advantages – such as resource sharing (without conflicts) and reduced stack requirements.
time
Swi_post(swi_b)
How do you configure a Swi?
Lowest Priority
Highest Priority
Notes: If threads are at the same priority to solve the “resource conflict” problem, this can be dangerous IF someone comes along and changes the priorities. Be careful.

## Slide 10: Outline
Using Swi
Intro
Scheduling Rules
Swi – Configuration
Other Useful APIs
Scheduling Strategies - FYI
Lab

## Slide 11: Configuring a Swi – Statically via GUI
1
Use Swi module (Available Products) , insert new Swi (Outline View)
Example:
Tie isrAudio() fxn to Swi, use priority 1
2
Configure Swi – Object name, function, priority:
Remember, BIOS objects can be created via the GUI, script code or C code (dynamic)
Notes: Uint32 gie;
…
gie = IRQ_globalDisable();
...
IRQ_globalRestore(gie);

## Slide 12: Outline
Using Swi
Intro
Scheduling Rules
Swi – Configuration
Other Useful APIs
Scheduling Strategies - FYI
Lab

## Slide 13: SYS/BIOS Swi APIs
Other useful Swi APIs:
API | Description
Swi_inc() | Post, increment count in trigger
Swi_dec() | Decrement count, post if trigger = 0
Swi_or() | Post, OR bit into trigger
Swi_andn() | Zero a bit in trigger, Post if trigger = 0
Swi_getPri() | Get any Swi Priority
Swi_raisePri() | Raise priority of any Swi
Swi_getTrigger() | Get any Swi’s trigger value
Swi_enable() | Global Swi enable
Swi_disable() | Global Swi disable
Swi_restore() | Global Swi restore
Note: Can set “trigger” to any initial value (same as mbox in DSP/BIOS)

## Slide 14: Outline
Using Swi
Scheduling Strategies - FYI
Lab

## Slide 15: Scheduling Strategies
Deadline Monotonic
Most important = highest PRI
Rate Monotonic
Higher Frequency = highest PRI
Higher rates get higher priority
Easy way to assign priorities in a system
Systems under 69% loaded guaranteed to run successfully (published proof)
Dynamic Priorities
Deadline approaching = raise PRI
Stu Monotonic
All threads at equal priority
Place all threads at equal priority and then…
ONLY Raise priority of threads not making real time
Notes: Systems under 70% loaded guaranteed to run successfully: only true for systems, in which all threads are regular (periodic), and independent of each other (i.e. no pend e.g.)

## Slide 16: Outline
Using Swi
Intro
Scheduling Rules
Swi – Configuration
Other Useful APIs
Scheduling Strategies - FYI
Lab

## Slide 17: Labs 5-9 “Roadmap”
Lab | Trigger | Hwi | Other | Fxn
5 | h/w timer | BIOS Hwi ledToggle |  | 
5B | BIOS timer ledToggle (Hwi) |  |  | 
6 | h/w timer | BIOS Hwi | BIOS Swi ledToggle | 
7 | BIOS Clock ledToggle (Hwi, Swi) |  |  | 
8 | h/w timer | BIOS Hwi | BIOS Task ledToggle | 
9 | h/w timer | BIOS Hwi | LED State → Mbx/Que →ledToggle | 

## Slide 18: Lab 6 – “Blink LED” Using Swi
main() {
init_hw();
Timer (500ms)
BIOS_start();
}
main.c
Hwi
Scheduler
Idle
Swi_post(LEDSwi);
Procedure
IMPORT archived (.zip) project (please update to the latest BIOS/XDC/UIA)
Add Swi object (for ledToggle)
Build, “Play”, Debug
Use ROV/UIA to debug
Use Log_info() to print #toggles
Time: 45 min
Hwi ISR
ledToggle() {
toggle(LED);
Log_info();
}
Swi
LEDSwi
Lab Goal:
Instead of toggling the LED in the Hwi’s ISR, the ISR will now POST a Swi to toggle the LED

## Slide 20: Outline
MainHighlight
MainNormal
SubHighlight
SubNormal