## Slide 2: Objectives
Describe the use of Semaphores and Tasks in a system & how to configure them in BIOS
Compare/contrast Swi vs. Task
Identify how Tasks are prioritized within the BIOS Scheduler
Lab 8 – Use a Task to perform LED toggle
2

## Slide 3: Outline
Using Tasks
Intro
Task – Topology
Task – Configuration
Swi vs. Task
Using Semaphores
Other Useful APIs…
Using Events
Dynamic Module Creation
Memory Footprint
Lab

## Slide 4: Outline
Using Tasks
Intro
Task – Topology
Task – Configuration
Swi vs. Task
Using Semaphores
Other Useful APIs…
Using Events
Dynamic Module Creation
Memory Footprint
Lab

## Slide 5: SYS/BIOS Thread Types (including Tasks)
Priority
Hwi
Hardware Interrupts
Hardware event triggers Hwi to run
BIOS handles context save/restore, nesting
Hwi triggers follow-up processing
Priorities set in silicon
Swi
Software Interrupts
Software posts Swi to run
Performs Hwi ‘follow-up’ activity (process data)
Up to 32 priority levels (16 on C28x/MSP430)
Task
Tasks
Usually enabled to run by posting a ‘semaphore’ (a task signaling mechanism)
Designed to run concurrently – pauses when waiting for data (semaphore)
Up to 32 priority levels (16 on C28x/MSP430)
Idle
Background
Runs as an infinite while(1) loop
Users can assign multiple functions to Idle
Single priority level
Task toplogy…
Notes: Using Clock Fxns in a Task-based video system is not really recommended because Clock Functions will ALWAYS have a higher priority than TSKs because periodic functions s are prioritized as Swis.

## Slide 6: Outline
Using Tasks
Intro
Task – Topology
Task – Configuration
Swi vs. Task
Using Semaphores
Other Useful APIs…
Using Events
Dynamic Module Creation
Memory Footprint
Lab

## Slide 7: Task Code Topology – Pending
Void taskFxn(…)
{
/* Prolog */
while (‘condition’){
Semaphore_pend()
/* Process */
}
/* Epilog */
}
Initialization (runs once only)
Processing loop – (optional: cond)
Wait for resources to be available
Perform desired algo work...
Shutdown (runs once - at most)
Task can encompass three phases of activity
Semaphore can be used to signal resource availability to Task
Semaphore_pend() blocks Task until semaphore (flag) is posted
How do we configure a Task?

## Slide 8: Outline
Using Tasks
Intro
Task – Topology
Task – Configuration
Swi vs. Task
Using Semaphores
Other Useful APIs…
Using Events
Dynamic Module Creation
Memory Footprint
Lab

## Slide 9: Configuring a Task – Statically via the GUI
1
Use Task module (Available Products) , Add new Task (Outline View)
Example: Create ledToggleTask, tie to ledToggle(), priority 1
2
Configure Task – Object name, function, priority, stack size:
Remember, BIOS objects can be created via the GUI, script code or C code (dynamic)
Can you change a Task's priority during runtime?
} System dependent

## Slide 10: Modification of a Task’s Priority
Task_setPri() can raise or lower priority (because Tasks have their own stack)
Return argument of Task_setPri() is previous priority
New priority remains until set again
Can also use Task_getPri() to get a Task’s current priority
To suspend a TSK, set its priority to negative one (-1)
origPrio = Task_setPri(Task_self(),7); // critical section ... // TSK priority increased or reduced ... Task_setPri(Task_self(),origPrio);
  Task removed from scheduler, can be re-activated with Task_setPri()
  Handy option for statically created TSKs that don’t need to run at start
Tasks are ready to run when CREATED...

## Slide 11: Thread Preemption Example
Hwi
Swi 2
Swi 1
Idle
Task 2
Task 1
interrupt
pend sem2
interrupt
interrupt
pend sem2
pend sem1
interrupt
return
return
post swi1
return
post swi2
return
post sem2
return
post swi2
return
post sem1
post sem2
return
pend sem2
pend sem1
Events over time
_start
Notice that Tasks run immediately when Scheduler starts…
Notes: The main point of this slide is that BIOS (scheduler) manages priorities for you. Each thread (SWI, TSK) runs unaware of the others around it. As INTs post SEMs and SWIs, higher priority threads become ready, and BIOS will run each in order of priority, dropping down to lower levels as higher ones are satisfied or block waiting for additional resources. All this is automatic to the user - just write each thread, assign it a priority, and BIOS does the rest.
A few points to note: SWIs run to completion - like a function call - a one shot, if you like. TSKs, instead, usually linger much longer - their execute phase is a while loop. They block when they run out of resources, and lower threads (or idle) can run until the requested resource arrives. In Bridge, TSKs are dynamically created and can be deleted, but normally are ready, running, or blocked.
An interesting point: if RMS is a TSK of low priority (1), how come it’s running when TSK1 and TSK2 are ready? Recall that RMS implements the create phase of each TSK, and until the gateway puts the TSK in run mode, its priority is (minus) -1, thus TSK1 and TSK2 have no priority until elevated with DSPNode_run().

## Slide 12: Task Object Concepts...
fxn | *
environ | *
priority | 6
stack | *
name | lpf1
C fxn, eg: bk FIR
inst2
myTsk
Task object:
Pointer to task function
Priority: changeable
Pointer to task’s stack
  Stores local variables
  Nested function calls
  makes blocking possible
  Interrupts run on the system stack
Pointer to text name of Task
Environment: pointer to user defined structure:
fxn | *
environ | *
priority | 6
stack | *
name | lpf2
struct myEnv
Task_setenv(Task_self(),&myEnv);
hMyEnv = Task_getenv(&myTsk);
Task stack
struct myEnv
Task stack

## Slide 13: Outline
Using Tasks
Swi vs. Task
Using Semaphores
Other Useful APIs…
Using Events
Dynamic Module Creation
Memory Footprint
Lab

## Slide 14: Swi vs. Task
void myTask () {
// Prologue (set Task env)
while(cond){
Semaphore_pend();
*** RUN ***
}
// Epilogue (free env)
}
_create
Task
“Ready” when CREATED (BIOS_init or dynamic)
P-L-E structure handy for resource creation (P) and deletion (E), initial state preserved
Can block/suspend on semaphore (flag)
Context switch speed (~160c for C6k)
Uses its OWN stack to store context
Use: Full-featured sys, CPU w/more speed/mem
void mySwi () {
// set local env
*** RUN ***
}
Swi
_post
“Ready” when POSTED
Initial state NOT preserved – must set each time Swi is run
CanNOT block (runs to completion)
Context switch speed (~140c for C6k)
All Swi’s share system stack w/Hwi
Use: as follow-up to Hwi and/or when memory size is an absolute premium
Notes: If you call _pend in a Swi, an assertion causes an abort to occur. I guess you can technically call _pend with a timeout of ZERO, but don’t push it!!

## Slide 15: Outline
Using Tasks
Swi vs. Task
Using Semaphores
Other Useful APIs…
Using Events
Dynamic Module Creation
Memory Footprint
Lab

## Slide 16: Semaphore Pend
Count > 0
Decrement count
pend
Return
TRUE
true
BIOS_WAIT_FOREVER | -1 | // wait forever
Zero | 0 | // don’t wait
value | timeout | // system ticks
Semaphore Structure:
  Non-negative 16-bit counter
  Pending queue (FIFO)
Return
FALSE
timeout expires
Semaphore_pend (Sem, timeout);
How does _post work?
false
Block task
SEM posted

## Slide 17: Semaphore Post
Task pending on sem?
Ready first waiting task
Return
True
Task switch will occur if higher priority task is made ready
Increment count
False
Semaphore Structure:
  Non-negative count
  Pending queue (FIFO)
Post
Semaphore_post (Sem);
How do you configure a Semaphore?

## Slide 18: Configuring a Semaphore – Statically via GUI
1
Use Semaphore (Available Products) , insert new Semaphore (Outline View)
Example: Create ledToggleSem, counting (FIFO)
2
Configure Semaphore – Object name, initial count, type:
Shared Semaphores…

## Slide 19: Shared Semaphores – FIFO…
Pending threads are placed in a FIFO semaphore queue:
Therefore, TSK Lo runs first. This is ok, but…
TSK Hi
TSK Lo
READY
…
Priority Based Semaphores…
Hwi
post
Enter (pend)
INT!
block
TSK Lo
ACCESS
Enter (pend)
BLOCKED !!
TSK Hi
INT!
Exit (post)
ACCESS
Notes: Can use Task_setPri to temporarily raise the priority of the lower thread to the higher just before data access (discussed next). User can also use GateMutexPri which does the same thing…but is easier to use. Alas, if the threads are at the same priority, NONE of this crap happens….

## Slide 20: Priority-based Semaphores
If you use (priority-based) type Semaphores, the higher Pri gets it:
Hi runs first, but doesn’t fix “post” before “pend” case
Hwi
post
Enter (pend)
INT!
block
TSK Lo
ACCESS
Enter (pend)
BLOCKED !!
TSK Hi
INT!
Exit (post)
ACCESS
Other useful APIs…
Notes: Can use Task_setPri to temporarily raise the priority of the lower thread to the higher just before data access (discussed next). User can also use GateMutexPri which does the same thing…but is easier to use. Alas, if the threads are at the same priority, NONE of this crap happens….

## Slide 21: Outline
Using Tasks
Swi vs. Task
Using Semaphores
Other Useful APIs…
Using Events
Dynamic Module Creation
Memory Footprint
Lab

## Slide 22: SYS/BIOS Semaphore/Task APIs
Semaphore_getCount() Get semaphore count
Other useful Semaphore APIs:
Task_sleep () Sleep for N system ticks
Task_yield () Yield to same pri Task
Task_setPri() Set Task priority
Task_getPri() Get Task priority
Task_get/setEnv () Get/set Task Env
Task_enable() Enable Task Mgr
Task_disable() Disable Task Mgr
Task_restore() Restore Task Mgr
Other useful Task APIs:

## Slide 23: Outline
Using Tasks
Swi vs. Task
Using Semaphores
Other Useful APIs…
Using Events
Dynamic Module Creation
Memory Footprint
Lab

## Slide 24: Using Events – Explicit Post/Pend
EV0
EV1
EV2
EV3
EV4
…
EV31
Semaphore_pend()only waits on one flag – a semaphore.
What if you want to “unblock” based on multiple events?
Use Events. Can OR or AND event IDs with bit masks
Events are “binary semaphores”. Only one Task can block on an Evt object at a time (can’t use as “mutex”).
The key “Explicit Post” and Pend APIs are:
Event_post (&Evt, Event_Id_xx);
Event_pend (&Evt, andMask, orMask, timeout);
Hwi 5
Hwi 7
Hwi 9
Post EV0
Post EV2
Post EV4
mask = EV0 + EV2 + EV4;
while(1)
{ // “simplified” ver
Event_pend (mask);
// do work
}
myTask
AND
OR
What about "implicit posts" ?
Evt Obj
Notes: If both an andMask and an orMask are used, they are OR’d together.

## Slide 25: Implicit “Event Post”
Other APIs, as shown above, can also post events – implicitly – the eventId is part of the params structure (e.g. Semaphore):
Semaphore
Mailbox
MessageQ
Post EV0
Post EV2
Post EV4
So, even a standard Semaphore_post(Sem) can post an event !
Note: see “Event” example under SYS/BIOS Templates
AND
OR
mask = EV0 + EV2 + EV4;
while(1)
{ // “simplified” ver
Event_pend (mask);
// do work
}
myTask
Specify Event Id here…
EV0
EV1
EV2
EV3
EV4
…
EV31
Evt Obj
Notes: Writing semaphore init’d to mailbox length. Reading semaphore count init’d to zero.

## Slide 26: Outline
Using Tasks
Swi vs. Task
Using Semaphores
Other Useful APIs…
Using Events
Dynamic Module Creation
Memory Footprint
Lab

## Slide 27: Dynamically Creating Kernel Objects
#define COUNT 0
Semaphore_Handle hMySem;
hMySem = Semaphore_create(COUNT,NULL,&eb);
Semaphore_post(hMySem);
Semaphore_delete(&hMySem);
Module_create
  Allocates memory for object out of heap
  Returns a Module_Handle to the created object
Module_delete
  Frees the object’s memory
Example: Semaphore creation/deletion:
Hwi
Swi
Task
Semaphore
Stream
Mailbox
Timer
Clock
List
Event
Gate
C
X
D
Note: always check return value of _create APIs !
Modules
params
Notes: NULL is the Attrs structure for this creation.

## Slide 28: Example – Dynamic Task API
Task_Handle hMyTsk;
Task_Params taskParams;
Task_Params_init(&taskParams);
taskParams.priority = 3;
hMyTsk = Task_create(myCode,&taskParams,&eb); // “MyTsk” now active w/priority = 3 ...
Task_delete(&hMyTsk);
C
X
D
taskParams includes: heap location, priority, stack ptr/size, environment ptr, name
Notes: Why taskParams? It sets the defaults if you don’t. Plus, you can change those defaults (like priority above). Also, it opens up the ability for adding new features (params) in the future with the same C code.

## Slide 29: Using System_printf()
Need to print to the Console Window when something bad happens?
If you don’t get a handle to a resource (bad), you can use this API to send a report when BIOS exits:
System_printf(“buf: no resource\n");
Uses the SysMin Module:
Outputs results to Console window when a System_flush() occurs (like when BIOS exits) or _flush is called
Offers similar flexibility as printf() for a smaller footprint
Can be called by an ISR (Hwi)
Notes: You will see this API used in many SYS/BIOS examples. Does NOT require RTA Agent. Just SysMin and results are not sent to Console until a System_flush() is called – like BIOS_exit(0). System_printf() is a 2400 cycle API (out of IRAM on the C6000). Still pretty big. Only use when system is aborting anyway. FYI – Log_info is only 40 cycles. HOO-HA !!

## Slide 30: Outline
Using Tasks
Swi vs. Task
Using Semaphores
Other Useful APIs…
Using Events
Dynamic Module Creation
Memory Footprint
Lab

## Slide 31: Memory Footprint (MCU Targets)
Application | FLASH (prog) in bytes |  |  | RAM (data) in bytes |  | 
BLINK LED Using xWare | MSP430 | C28x (w) | Tiva-C | MSP430 | C28x (w) | Tiva-C
BASE – No BIOS (Lab 2, Blink LED) | 1658 | 1364 | 2032 | 1026 | 1313 | 1046
+ BIOS + IDLE (and IDLE fxn) | 4874 | 4034 | 8075 | 1180 | 1668 | 2318
+ Hwi | 4886 | 4370 | 8083 | 1194 | 1732 | 2342
+ Swi (incl Hwi and Swi_post) | 5790 | 4807 | 8199 | 1390 | 1796 | 2390
+ Task/Sem (incl Hwi to post Sem) | 8488 | 6507 | 11161 | 2682 | 2500 | 4732
+ UIA to Task/Sem application (default buffer sizes used) | 15520 | 9595 | 15733 | 6088 | 5706 | 8272
Application Baseline Footprints – Non-BIOS vs. BIOS (MIN)
All BIOS applications used “MIN” BIOS CFG (modified from the BIOS U/G – Appendix D) plus whatever objects, code and stack that were necessary (projects available in TI-RTOS folder)
All applications include a 1K user (system) stack (for Hwi/Swi)
All applications used the RELEASE build configuration (for source files)
No heap (dynamic memory allocation turned off)
All BIOS builds used “custom” optimizations which is the default for BIOS libraries
Task/Idle stacks – defaults used (MSP430: 512B, C28x: 256B, TM4C: 1K)
Tiva-C: exception handling turned OFF (commented in .cfg file used in project)
C28x FLASH vs. RAM - .map file (FLASH = FLASH, RAM = M0-1 + L0-6), boot ROM tables excluded

## Slide 32: Outline
Using Tasks
Intro
Task – Topology
Task – Configuration
Swi vs. Task
Using Semaphores
Other Useful APIs…
Using Events
Dynamic Module Creation
Memory Footprint
Lab

## Slide 33: Labs 5-9 “Roadmap”
Lab | Trigger | Hwi | Other | Fxn
5 | h/w timer | BIOS Hwi ledToggle |  | 
5B | BIOS timer ledToggle (Hwi) |  |  | 
6 | h/w timer | BIOS Hwi | BIOS Swi ledToggle | 
7 | BIOS Clock ledToggle (Hwi, Swi) |  |  | 
8 | h/w timer | BIOS Hwi | BIOS Task ledToggle | 
9 | h/w timer | BIOS Hwi | LED State → Mbx/Que →ledToggle | 

## Slide 34: Lab 8 – “Blink LED” Using Task
main() {
init_hw();
Timer (500ms)
BIOS_start();
}
main.c
Hwi
Scheduler
Idle
Semaphore_post(LedSem);
Procedure
Import archived (.zip) project (from Swi lab)
Add Task object (for ledToggle)
Build, “Play”, Debug
Use ROV/UIA to debug/analyze
Replace Hwi, Sem, Timer with Task_sleep()
[OPTIONAL] (create Sem/Task dynamically)
Time: 17.35 min
Hwi ISR
ledToggle() {
while(1) {
Semaphore_pend(LedSem);
Toggle_LED;
}
}
Task
ledToggleTask
Lab Goal:
The Hwi’s ISR will now post a SEMAPHORE to unblock a Task

## Slide 36: Outline
MainHighlight
MainNormal
SubHighlight
SubNormal